https://github.com/qemu/qemu/blob/master/docs/interop/qcow2.txt

== General ==

A qcow2 image file is organized in units of constant size, which are called
(host) clusters. A cluster is the unit in which all allocations are done,
both for actual guest data and for image metadata.

Likewise, the virtual disk as seen by the guest is divided into (guest)
clusters of the same size.

All numbers in qcow2 are stored in Big Endian byte order.

== Header ==

The first cluster of a qcow2 image contains the file header:

    Byte 0 - 3: magic
        QCOW magic string ("QFI\xfb")

        4 - 7: version
        Version number (valid values are 2 and 3)

        8 - 15: backing_file_offset
        Offset into the image file at which the backing file name
        is stored (NB: The string is not null terminated). 0 if the
        image doesn't have a backing file.

        Note: backing files are incompatible with raw external data
        files (auto-clear feature bit 1).

        16 - 19: backing_file_size
        Length of the backing file name in bytes. Must not be
        longer than 1023 bytes. Undefined if the image doesn't have
        a backing file.

        20 - 23: cluster_bits
        Number of bits that are used for addressing an offset
        within a cluster (1 << cluster_bits is the cluster size).
        Must not be less than 9 (i.e. 512 byte clusters).(2^9)

        Note: qemu as of today has an implementation limit of 2 MB
        as the maximum cluster size and won't be able to open images
        with larger cluster sizes.

        Note: if the image has Extended L2 Entries then cluster_bits
        must be at least 14 (i.e. 16384 byte clusters).

        24 - 31: size
        Virtual disk size in bytes.

        Note: qemu has an implementation limit of 32 MB as
        the maximum L1 table size. With a 2 MB cluster
        size, it is unable to populate a virtual cluster
        beyond 2 EB (61 bits); with a 512 byte cluster
        size, it is unable to populate a virtual size
        larger than 128 GB (37 bits). Meanwhile, L1/L2
        table layouts limit an image to no more than 64 PB
        (56 bits) of populated clusters, and an image may
        hit other limits first (such as a file system's
        maximum size).

        32 - 35: crypt_method
        0 for no encryption
        1 for AES encryption
        2 for LUKS encryption

        36 - 39: l1_size
        Number of entries in the active L1 table

        40 - 47: l1_table_offset
        Offset into the image file at which the active L1 table
        starts. Must be aligned to a cluster boundary.

        48 - 55: refcount_table_offset
        Offset into the image file at which the refcount table
        starts. Must be aligned to a cluster boundary.

        56 - 59: refcount_table_clusters
        Number of clusters that the refcount table occupies

        60 - 63: nb_snapshots
        Number of snapshots contained in the image

        64 - 71: snapshots_offset
        Offset into the image file at which the snapshot table
        starts. Must be aligned to a cluster boundary.

For version 2, the header is exactly 72 bytes in length, and finishes here.
For version 3 or higher, the header length is at least 104 bytes, including
the next fields through header_length.

        72 - 79: incompatible_features
        Bitmask of incompatible features. An implementation must
        fail to open an image if an unknown bit is set.

        Bit 0: Dirty bit. If this bit is set then refcounts
        may be inconsistent, make sure to scan L1/L2
        tables to repair refcounts before accessing the
        image.

        Bit 1: Corrupt bit. If this bit is set then any data
        structure may be corrupt and the image must not
        be written to (unless for regaining
        consistency).

        Bit 2: External data file bit. If this bit is set, an
        external data file is used. Guest clusters are
        then stored in the external data file. For such
        images, clusters in the external data file are
        not refcounted. The offset field in the
        Standard Cluster Descriptor must match the
        guest offset and neither compressed clusters
        nor internal snapshots are supported.

        An External Data File Name header extension may
        be present if this bit is set.

        Bit 3: Compression type bit. If this bit is set,
        a non-default compression is used for compressed
        clusters. The compression_type field must be
        present and not zero.

        Bit 4: Extended L2 Entries. If this bit is set then
        L2 table entries use an extended format that
        allows subcluster-based allocation. See the
        Extended L2 Entries section for more details.

        Bits 5-63: Reserved (set to 0)

        80 - 87: compatible_features
        Bitmask of compatible features. An implementation can
        safely ignore any unknown bits that are set.

        Bit 0: Lazy refcounts bit. If this bit is set then
        lazy refcount updates can be used. This means
        marking the image file dirty and postponing
        refcount metadata updates.

        Bits 1-63: Reserved (set to 0)

        88 - 95: autoclear_features
        Bitmask of auto-clear features. An implementation may only
        write to an image with unknown auto-clear features if it
        clears the respective bits from this field first.

        Bit 0: Bitmaps extension bit
        This bit indicates consistency for the bitmaps
        extension data.

        It is an error if this bit is set without the
        bitmaps extension present.

        If the bitmaps extension is present but this
        bit is unset, the bitmaps extension data must be
        considered inconsistent.

        Bit 1: Raw external data bit
        If this bit is set, the external data file can
        be read as a consistent standalone raw image
        without looking at the qcow2 metadata.

        Setting this bit has a performance impact for
        some operations on the image (e.g. writing
        zeros requires writing to the data file instead
        of only setting the zero flag in the L2 table
        entry) and conflicts with backing files.

        This bit may only be set if the External Data
        File bit (incompatible feature bit 1) is also
        set.

        Bits 2-63: Reserved (set to 0)

        96 - 99: refcount_order
        Describes the width of a reference count block entry (width
        in bits: refcount_bits = 1 << refcount_order). For version 2
        images, the order is always assumed to be 4
        (i.e. refcount_bits = 16).
        This value may not exceed 6 (i.e. refcount_bits = 64).

        100 - 103: header_length
        Length of the header structure in bytes. For version 2
        images, the length is always assumed to be 72 bytes.
        For version 3 it's at least 104 bytes and must be a multiple
        of 8.

=== Additional fields (version 3 and higher) ===

In general, these fields are optional and may be safely ignored by the software,
as well as filled by zeros (which is equal to field absence), if software needs
to set field B, but does not care about field A which precedes B. More
formally, additional fields have the following compatibility rules:

1. If the value of the additional field must not be ignored for correct
handling of the file, it will be accompanied by a corresponding incompatible
feature bit.

2. If there are no unrecognized incompatible feature bits set, an unknown
additional field may be safely ignored other than preserving its value when
rewriting the image header.

3. An explicit value of 0 will have the same behavior as when the field is not
present*, if not altered by a specific incompatible bit.

*. A field is considered not present when header_length is less than or equal
to the field's offset. Also, all additional fields are not present for
version 2.

        104: compression_type

        Defines the compression method used for compressed clusters.
        All compressed clusters in an image use the same compression
        type.

        If the incompatible bit "Compression type" is set: the field
        must be present and non-zero (which means non-zlib
        compression type). Otherwise, this field must not be present
        or must be zero (which means zlib).

        Available compression type values:
        0: zlib <https://www.zlib.net/>
        1: zstd <http://github.com/facebook/zstd>

=== Header padding ===

@header_length must be a multiple of 8, which means that if the end of the last
additional field is not aligned, some padding is needed. This padding must be
zeroed, so that if some existing (or future) additional field will fall into
the padding, it will be interpreted accordingly to point [3.] of the previous
paragraph, i.e. in the same manner as when this field is not present.

=== Header extensions ===

Directly after the image header, optional sections called header extensions can
be stored. Each extension has a structure like the following:

    Byte 0 - 3: Header extension type:
        0x00000000 - End of the header extension area
        0xe2792aca - Backing file format name string
        0x6803f857 - Feature name table
        0x23852875 - Bitmaps extension
        0x0537be77 - Full disk encryption header pointer
        0x44415441 - External data file name string
        other - Unknown header extension, can be safely
        ignored

        4 - 7: Length of the header extension data

        8 - n: Header extension data

        n - m: Padding to round up the header extension size to the next
        multiple of 8.

Unless stated otherwise, each header extension type shall appear at most once
in the same image.

If the image has a backing file then the backing file name should be stored in
the remaining space between the end of the header extension area and the end of
the first cluster. It is not allowed to store other data here, so that an
implementation can safely modify the header and add extensions without harming
data of compatible features that it doesn't support. Compatible features that
need space for additional data can use a header extension.

== String header extensions ==

Some header extensions (such as the backing file format name and the external
data file name) are just a single string. In this case, the header extension
length is the string length and the string is not '\0' terminated. (The header
extension padding can make it look like a string is '\0' terminated, but
neither is padding always necessary nor is there a guarantee that zero bytes
are used for padding.)

== Feature name table ==

The feature name table is an optional header extension that contains the name
for features used by the image. It can be used by applications that don't know
the respective feature (e.g. because the feature was introduced only later) to
display a useful error message.

The number of entries in the feature name table is determined by the length of
the header extension data. Each entry look like this:

    Byte 0: Type of feature (select feature bitmap)
        0: Incompatible feature
        1: Compatible feature
        2: Autoclear feature

        1: Bit number within the selected feature bitmap (valid
        values: 0-63)

        2 - 47: Feature name (padded with zeros, but not necessarily null
        terminated if it has full length)

== Bitmaps extension ==

The bitmaps extension is an optional header extension. It provides the ability
to store bitmaps related to a virtual disk. For now, there is only one bitmap
type: the dirty tracking bitmap, which tracks virtual disk changes from some
point in time.

The data of the extension should be considered consistent only if the
corresponding auto-clear feature bit is set, see autoclear_features above.

The fields of the bitmaps extension are:

    Byte 0 - 3: nb_bitmaps
        The number of bitmaps contained in the image. Must be
        greater than or equal to 1.

        Note: QEMU currently only supports up to 65535 bitmaps per
        image.

        4 - 7: Reserved, must be zero.

        8 - 15: bitmap_directory_size
        Size of the bitmap directory in bytes. It is the cumulative
        size of all (nb_bitmaps) bitmap directory entries.

        16 - 23: bitmap_directory_offset
        Offset into the image file at which the bitmap directory
        starts. Must be aligned to a cluster boundary.

== Full disk encryption header pointer ==

The full disk encryption header must be present if, and only if, the
'crypt_method' header requires metadata. Currently this is only true
of the 'LUKS' crypt method. The header extension must be absent for
other methods.

This header provides the offset at which the crypt method can store
its additional data, as well as the length of such data.

    Byte 0 - 7: Offset into the image file at which the encryption
        header starts in bytes. Must be aligned to a cluster
        boundary.
    Byte 8 - 15: Length of the written encryption header in bytes.
        Note actual space allocated in the qcow2 file may
        be larger than this value, since it will be rounded
        to the nearest multiple of the cluster size. Any
        unused bytes in the allocated space will be initialized
        to 0.

For the LUKS crypt method, the encryption header works as follows.

The first 592 bytes of the header clusters will contain the LUKS
partition header. This is then followed by the key material data areas.
The size of the key material data areas is determined by the number of
stripes in the key slot and key size. Refer to the LUKS format
specification ('docs/on-disk-format.pdf' in the cryptsetup source
package) for details of the LUKS partition header format.

In the LUKS partition header, the "payload-offset" field will be
calculated as normal for the LUKS spec. ie the size of the LUKS
header, plus key material regions, plus padding, relative to the
start of the LUKS header. This offset value is not required to be
qcow2 cluster aligned. Its value is currently never used in the
context of qcow2, since the qcow2 file format itself defines where
the real payload offset is, but none the less a valid payload offset
should always be present.

In the LUKS key slots header, the "key-material-offset" is relative
to the start of the LUKS header clusters in the qcow2 container,
not the start of the qcow2 file.

Logically the layout looks like

  +-----------------------------+
  | QCow2 header |
  | QCow2 header extension X |
  | QCow2 header extension FDE |
  | QCow2 header extension ... |
  | QCow2 header extension Z |
  +-----------------------------+
  | ....other QCow2 tables.... |
  . .
  . .
  +-----------------------------+
  | +-------------------------+ |
  | | LUKS partition header | |
  | +-------------------------+ |
  | | LUKS key material 1 | |
  | +-------------------------+ |
  | | LUKS key material 2 | |
  | +-------------------------+ |
  | | LUKS key material ... | |
  | +-------------------------+ |
  | | LUKS key material 8 | |
  | +-------------------------+ |
  +-----------------------------+
  | QCow2 cluster payload |
  . .
  . .
  . .
  | |
  +-----------------------------+

== Data encryption ==

When an encryption method is requested in the header, the image payload
data must be encrypted/decrypted on every write/read. The image headers
and metadata are never encrypted.

The algorithms used for encryption vary depending on the method

 - AES:

   The AES cipher, in CBC mode, with 256 bit keys.

   Initialization vectors generated using plain64 method, with
   the virtual disk sector as the input tweak.

   This format is no longer supported in QEMU system emulators, due
   to a number of design flaws affecting its security. It is only
   supported in the command line tools for the sake of back compatibility
   and data liberation.

 - LUKS:

   The algorithms are specified in the LUKS header.

   Initialization vectors generated using the method specified
   in the LUKS header, with the physical disk sector as the
   input tweak.

== Host cluster management ==

qcow2 manages the allocation of host clusters by maintaining a reference count
for each host cluster. A refcount of 0 means that the cluster is free, 1 means
that it is used, and >= 2 means that it is used and any write access must
perform a COW (copy on write) operation.

The refcounts are managed in a two-level table. The first level is called
refcount table and has a variable size (which is stored in the header). The
refcount table can cover multiple clusters, however it needs to be contiguous
in the image file.

It contains pointers to the second level structures which are called refcount
blocks and are exactly one cluster in size.

Although a large enough refcount table can reserve clusters past 64 PB
(56 bits) (assuming the underlying protocol can even be sized that
large), note that some qcow2 metadata such as L1/L2 tables must point
to clusters prior to that point.

Note: qemu has an implementation limit of 8 MB as the maximum refcount
table size. With a 2 MB cluster size and a default refcount_order of
4, it is unable to reference host resources beyond 2 EB (61 bits); in
the worst case, with a 512 cluster size and refcount_order of 6, it is
unable to access beyond 32 GB (35 bits).

Given an offset into the image file, the refcount of its cluster can be
obtained as follows:

    refcount_block_entries = (cluster_size * 8 / refcount_bits)

    refcount_block_index = (offset / cluster_size) % refcount_block_entries
    refcount_table_index = (offset / cluster_size) / refcount_block_entries

    refcount_block = load_cluster(refcount_table[refcount_table_index]);
    return refcount_block[refcount_block_index];

Refcount table entry:

    Bit 0 - 8: Reserved (set to 0)

        9 - 63: Bits 9-63 of the offset into the image file at which the
        refcount block starts. Must be aligned to a cluster
        boundary.

        If this is 0, the corresponding refcount block has not yet
        been allocated. All refcounts managed by this refcount block
        are 0.

Refcount block entry (x = refcount_bits - 1):

    Bit 0 - x: Reference count of the cluster. If refcount_bits implies a
        sub-byte width, note that bit 0 means the least significant
        bit in this context.

== Cluster mapping ==

Just as for refcounts, qcow2 uses a two-level structure for the mapping of
guest clusters to host clusters. They are called L1 and L2 table.

The L1 table has a variable size (stored in the header) and may use multiple
clusters, however it must be contiguous in the image file. L2 tables are
exactly one cluster in size.

The L1 and L2 tables have implications on the maximum virtual file
size; for a given L1 table size, a larger cluster size is required for
the guest to have access to more space. Furthermore, a virtual
cluster must currently map to a host offset below 64 PB (56 bits)
(although this limit could be relaxed by putting reserved bits into
use). Additionally, as cluster size increases, the maximum host
offset for a compressed cluster is reduced (a 2M cluster size requires
compressed clusters to reside below 512 TB (49 bits), and this limit
cannot be relaxed without an incompatible layout change).

Given an offset into the virtual disk, the offset into the image file can be
obtained as follows:

    l2_entries = (cluster_size / sizeof(uint64_t)) [*]

    l2_index = (offset / cluster_size) % l2_entries
    l1_index = (offset / cluster_size) / l2_entries

    l2_table = load_cluster(l1_table[l1_index]);
    cluster_offset = l2_table[l2_index];

    return cluster_offset + (offset % cluster_size)

    [*] this changes if Extended L2 Entries are enabled, see next section

L1 table entry:

    Bit 0 - 8: Reserved (set to 0)

        9 - 55: Bits 9-55 of the offset into the image file at which the L2
        table starts. Must be aligned to a cluster boundary. If the
        offset is 0, the L2 table and all clusters described by this
        L2 table are unallocated.

        56 - 62: Reserved (set to 0)

        63: 0 for an L2 table that is unused or requires COW, 1 if its
        refcount is exactly one. This information is only accurate
        in the active L1 table.

L2 table entry:

    Bit 0 - 61: Cluster descriptor

        62: 0 for standard clusters
        1 for compressed clusters

        63: 0 for clusters that are unused, compressed or require COW.
        1 for standard clusters whose refcount is exactly one.
        This information is only accurate in L2 tables
        that are reachable from the active L1 table.

        With external data files, all guest clusters have an
        implicit refcount of 1 (because of the fixed host = guest
        mapping for guest cluster offsets), so this bit should be 1
        for all allocated clusters.

Standard Cluster Descriptor:

    Bit 0: If set to 1, the cluster reads as all zeros. The host
        cluster offset can be used to describe a preallocation,
        but it won't be used for reading data from this cluster,
        nor is data read from the backing file if the cluster is
        unallocated.

        With version 2 or with extended L2 entries (see the next
        section), this is always 0.

        1 - 8: Reserved (set to 0)

        9 - 55: Bits 9-55 of host cluster offset. Must be aligned to a
        cluster boundary. If the offset is 0 and bit 63 is clear,
        the cluster is unallocated. The offset may only be 0 with
        bit 63 set (indicating a host cluster offset of 0) when an
        external data file is used.

        56 - 61: Reserved (set to 0)

Compressed Clusters Descriptor (x = 62 - (cluster_bits - 8)):

    Bit 0 - x-1: Host cluster offset. This is usually _not_ aligned to a
        cluster or sector boundary! If cluster_bits is
        small enough that this field includes bits beyond
        55, those upper bits must be set to 0.

        x - 61: Number of additional 512-byte sectors used for the
        compressed data, beyond the sector containing the offset
        in the previous field. Some of these sectors may reside
        in the next contiguous host cluster.

        Note that the compressed data does not necessarily occupy
        all of the bytes in the final sector; rather, decompression
        stops when it has produced a cluster of data.

        Another compressed cluster may map to the tail of the final
        sector used by this compressed cluster.

If a cluster is unallocated, read requests shall read the data from the backing
file (except if bit 0 in the Standard Cluster Descriptor is set). If there is
no backing file or the backing file is smaller than the image, they shall read
zeros for all parts that are not covered by the backing file.

== Extended L2 Entries ==

An image uses Extended L2 Entries if bit 4 is set on the incompatible_features
field of the header.

In these images standard data clusters are divided into 32 subclusters of the
same size. They are contiguous and start from the beginning of the cluster.
Subclusters can be allocated independently and the L2 entry contains information
indicating the status of each one of them. Compressed data clusters don't have
subclusters so they are treated the same as in images without this feature.

The size of an extended L2 entry is 128 bits so the number of entries per table
is calculated using this formula:

    l2_entries = (cluster_size / (2 * sizeof(uint64_t)))

The first 64 bits have the same format as the standard L2 table entry described
in the previous section, with the exception of bit 0 of the standard cluster
descriptor.

The last 64 bits contain a subcluster allocation bitmap with this format:

Subcluster Allocation Bitmap (for standard clusters):

    Bit 0 - 31: Allocation status (one bit per subcluster)

        1: the subcluster is allocated. In this case the
        host cluster offset field must contain a valid
        offset.
        0: the subcluster is not allocated. In this case
        read requests shall go to the backing file or
        return zeros if there is no backing file data.

        Bits are assigned starting from the least significant
        one (i.e. bit x is used for subcluster x).

        32 - 63 Subcluster reads as zeros (one bit per subcluster)

        1: the subcluster reads as zeros. In this case the
        allocation status bit must be unset. The host
        cluster offset field may or may not be set.
        0: no effect.

        Bits are assigned starting from the least significant
        one (i.e. bit x is used for subcluster x - 32).

Subcluster Allocation Bitmap (for compressed clusters):

    Bit 0 - 63: Reserved (set to 0)
        Compressed clusters don't have subclusters,
        so this field is not used.

== Snapshots ==

qcow2 supports internal snapshots. Their basic principle of operation is to
switch the active L1 table, so that a different set of host clusters are
exposed to the guest.

When creating a snapshot, the L1 table should be copied and the refcount of all
L2 tables and clusters reachable from this L1 table must be increased, so that
a write causes a COW and isn't visible in other snapshots.

When loading a snapshot, bit 63 of all entries in the new active L1 table and
all L2 tables referenced by it must be reconstructed from the refcount table
as it doesn't need to be accurate in inactive L1 tables.

A directory of all snapshots is stored in the snapshot table, a contiguous area
in the image file, whose starting offset and length are given by the header
fields snapshots_offset and nb_snapshots. The entries of the snapshot table
have variable length, depending on the length of ID, name and extra data.

Snapshot table entry:

    Byte 0 - 7: Offset into the image file at which the L1 table for the
        snapshot starts. Must be aligned to a cluster boundary.

        8 - 11: Number of entries in the L1 table of the snapshots

        12 - 13: Length of the unique ID string describing the snapshot

        14 - 15: Length of the name of the snapshot

        16 - 19: Time at which the snapshot was taken in seconds since the
        Epoch

        20 - 23: Subsecond part of the time at which the snapshot was taken
        in nanoseconds

        24 - 31: Time that the guest was running until the snapshot was
        taken in nanoseconds

        32 - 35: Size of the VM state in bytes. 0 if no VM state is saved.
        If there is VM state, it starts at the first cluster
        described by first L1 table entry that doesn't describe a
        regular guest cluster (i.e. VM state is stored like guest
        disk content, except that it is stored at offsets that are
        larger than the virtual disk presented to the guest)

        36 - 39: Size of extra data in the table entry (used for future
        extensions of the format)

        variable: Extra data for future extensions. Unknown fields must be
        ignored. Currently defined are (offset relative to snapshot
        table entry):

        Byte 40 - 47: Size of the VM state in bytes. 0 if no VM
        state is saved. If this field is present,
        the 32-bit value in bytes 32-35 is ignored.

        Byte 48 - 55: Virtual disk size of the snapshot in bytes

        Byte 56 - 63: icount value which corresponds to
        the record/replay instruction count
        when the snapshot was taken. Set to -1
        if icount was disabled

        Version 3 images must include extra data at least up to
        byte 55.

        variable: Unique ID string for the snapshot (not null terminated)

        variable: Name of the snapshot (not null terminated)

        variable: Padding to round up the snapshot table entry size to the
        next multiple of 8.

== Bitmaps ==

As mentioned above, the bitmaps extension provides the ability to store bitmaps
related to a virtual disk. This section describes how these bitmaps are stored.

All stored bitmaps are related to the virtual disk stored in the same image, so
each bitmap size is equal to the virtual disk size.

Each bit of the bitmap is responsible for strictly defined range of the virtual
disk. For bit number bit_nr the corresponding range (in bytes) will be:

    [bit_nr * bitmap_granularity .. (bit_nr + 1) * bitmap_granularity - 1]

Granularity is a property of the concrete bitmap, see below.

=== Bitmap directory ===

Each bitmap saved in the image is described in a bitmap directory entry. The
bitmap directory is a contiguous area in the image file, whose starting offset
and length are given by the header extension fields bitmap_directory_offset and
bitmap_directory_size. The entries of the bitmap directory have variable
length, depending on the lengths of the bitmap name and extra data.

Structure of a bitmap directory entry:

    Byte 0 - 7: bitmap_table_offset
        Offset into the image file at which the bitmap table
        (described below) for the bitmap starts. Must be aligned to
        a cluster boundary.

        8 - 11: bitmap_table_size
        Number of entries in the bitmap table of the bitmap.

        12 - 15: flags
        Bit
        0: in_use
        The bitmap was not saved correctly and may be
        inconsistent. Although the bitmap metadata is still
        well-formed from a qcow2 perspective, the metadata
        (such as the auto flag or bitmap size) or data
        contents may be outdated.

        1: auto
        The bitmap must reflect all changes of the virtual
        disk by any application that would write to this qcow2
        file (including writes, snapshot switching, etc.). The
        type of this bitmap must be 'dirty tracking bitmap'.

        2: extra_data_compatible
        This flags is meaningful when the extra data is
        unknown to the software (currently any extra data is
        unknown to QEMU).
        If it is set, the bitmap may be used as expected, extra
        data must be left as is.
        If it is not set, the bitmap must not be used, but
        both it and its extra data be left as is.

        Bits 3 - 31 are reserved and must be 0.

        16: type
        This field describes the sort of the bitmap.
        Values:
        1: Dirty tracking bitmap

        Values 0, 2 - 255 are reserved.

        17: granularity_bits
        Granularity bits. Valid values: 0 - 63.

        Note: QEMU currently supports only values 9 - 31.

        Granularity is calculated as
        granularity = 1 << granularity_bits

        A bitmap's granularity is how many bytes of the image
        accounts for one bit of the bitmap.

        18 - 19: name_size
        Size of the bitmap name. Must be non-zero.

        Note: QEMU currently doesn't support values greater than
        1023.

        20 - 23: extra_data_size
        Size of type-specific extra data.

        For now, as no extra data is defined, extra_data_size is
        reserved and should be zero. If it is non-zero the
        behavior is defined by extra_data_compatible flag.

        variable: extra_data
        Extra data for the bitmap, occupying extra_data_size bytes.
        Extra data must never contain references to clusters or in
        some other way allocate additional clusters.

        variable: name
        The name of the bitmap (not null terminated), occupying
        name_size bytes. Must be unique among all bitmap names
        within the bitmaps extension.

        variable: Padding to round up the bitmap directory entry size to the
        next multiple of 8. All bytes of the padding must be zero.

=== Bitmap table ===

Each bitmap is stored using a one-level structure (as opposed to two-level
structures like for refcounts and guest clusters mapping) for the mapping of
bitmap data to host clusters. This structure is called the bitmap table.

Each bitmap table has a variable size (stored in the bitmap directory entry)
and may use multiple clusters, however, it must be contiguous in the image
file.

Structure of a bitmap table entry:

    Bit 0: Reserved and must be zero if bits 9 - 55 are non-zero.
        If bits 9 - 55 are zero:
        0: Cluster should be read as all zeros.
        1: Cluster should be read as all ones.

        1 - 8: Reserved and must be zero.

        9 - 55: Bits 9 - 55 of the host cluster offset. Must be aligned to
        a cluster boundary. If the offset is 0, the cluster is
        unallocated; in that case, bit 0 determines how this
        cluster should be treated during reads.

        56 - 63: Reserved and must be zero.

=== Bitmap data ===

As noted above, bitmap data is stored in separate clusters, described by the
bitmap table. Given an offset (in bytes) into the bitmap data, the offset into
the image file can be obtained as follows:

    image_offset(bitmap_data_offset) =
        bitmap_table[bitmap_data_offset / cluster_size] +
        (bitmap_data_offset % cluster_size)

This offset is not defined if bits 9 - 55 of bitmap table entry are zero (see
above).

Given an offset byte_nr into the virtual disk and the bitmap's granularity, the
bit offset into the image file to the corresponding bit of the bitmap can be
calculated like this:

    bit_offset(byte_nr) =
        image_offset(byte_nr / granularity / 8) * 8 +
        (byte_nr / granularity) % 8

If the size of the bitmap data is not a multiple of the cluster size then the
last cluster of the bitmap data contains some unused tail bits. These bits must
be zero.

=== Dirty tracking bitmaps ===

Bitmaps with 'type' field equal to one are dirty tracking bitmaps.

When the virtual disk is in use dirty tracking bitmap may be 'enabled' or
'disabled'. While the bitmap is 'enabled', all writes to the virtual disk
should be reflected in the bitmap. A set bit in the bitmap means that the
corresponding range of the virtual disk (see above) was written to while the
bitmap was 'enabled'. An unset bit means that this range was not written to.

The software doesn't have to sync the bitmap in the image file with its
representation in RAM after each write or metadata change. Flag 'in_use'
should be set while the bitmap is not synced.

In the image file the 'enabled' state is reflected by the 'auto' flag. If this
flag is set, the software must consider the bitmap as 'enabled' and start
tracking virtual disk changes to this bitmap from the first write to the
virtual disk. If this flag is not set then the bitmap is disabled.

https://github.com/qemu/qemu/blob/master/docs/qcow2-cache.txt
qcow2 L2/refcount cache configuration
=====================================
Copyright (C) 2015, 2018-2020 Igalia, S.L.
Author: Alberto Garcia <berto@igalia.com>

This work is licensed under the terms of the GNU GPL, version 2 or
later. See the COPYING file in the top-level directory.

Introduction
------------
The QEMU qcow2 driver has two caches that can improve the I/O
performance significantly. However, setting the right cache sizes is
not a straightforward operation.

This document attempts to give an overview of the L2 and refcount
caches, and how to configure them.

Please refer to the docs/interop/qcow2.txt file for an in-depth
technical description of the qcow2 file format.

Clusters
--------
A qcow2 file is organized in units of constant size called clusters.

The cluster size is configurable, but it must be a power of two and
its value 512 bytes or higher. QEMU currently defaults to 64 KB
clusters, and it does not support sizes larger than 2MB. (aqui está o caso da qcow3 se é que existe)

The 'qemu-img create' command supports specifying the size using the
cluster_size option:

   qemu-img create -f qcow2 -o cluster_size=128K hd.qcow2 4G

The L2 tables
-------------
The qcow2 format uses a two-level structure to map the virtual disk as
seen by the guest to the disk image in the host. These structures are
called the L1 and L2 tables.

There is one single L1 table per disk image. The table is small and is
always kept in memory.

There can be many L2 tables, depending on how much space has been
allocated in the image. Each table is one cluster in size. In order to
read or write data from the virtual disk, QEMU needs to read its
corresponding L2 table to find out where that data is located. Since
reading the table for each I/O operation can be expensive, QEMU keeps
an L2 cache in memory to speed up disk access.

The size of the L2 cache can be configured, and setting the right
value can improve the I/O performance significantly.

The refcount blocks
-------------------
The qcow2 format also maintains a reference count for each cluster.
Reference counts are used for cluster allocation and internal
snapshots. The data is stored in a two-level structure similar to the
L1/L2 tables described above.

The second level structures are called refcount blocks, are also one
cluster in size and the number is also variable and dependent on the
amount of allocated space.

Each block contains a number of refcount entries. Their size (in bits)
is a power of two and must not be higher than 64. It defaults to 16
bits, but a different value can be set using the refcount_bits option:

   qemu-img create -f qcow2 -o refcount_bits=8 hd.qcow2 4G

QEMU keeps a refcount cache to speed up I/O much like the
aforementioned L2 cache, and its size can also be configured.

Choosing the right cache sizes
------------------------------
In order to choose the cache sizes we need to know how they relate to
the amount of allocated space.

The part of the virtual disk that can be mapped by the L2 and refcount
caches (in bytes) is:

   disk_size = l2_cache_size * cluster_size / 8
   disk_size = refcount_cache_size * cluster_size * 8 / refcount_bits

With the default values for cluster_size (64KB) and refcount_bits
(16), this becomes:

   disk_size = l2_cache_size * 8192
   disk_size = refcount_cache_size * 32768

So in order to cover n GB of disk space with the default values we
need:

   l2_cache_size = disk_size_GB * 131072
   refcount_cache_size = disk_size_GB * 32768

For example, 1MB of L2 cache is needed to cover every 8 GB of the virtual
image size (given that the default cluster size is used):

   8 GB / 8192 = 1 MB

The refcount cache is 4 times the cluster size by default. With the default
cluster size of 64 KB, it is 256 KB (262144 bytes). This is sufficient for
8 GB of image size:

   262144 * 32768 = 8 GB

How to configure the cache sizes
--------------------------------
Cache sizes can be configured using the -drive option in the
command-line, or the 'blockdev-add' QMP command.

There are three options available, and all of them take bytes:

"l2-cache-size": maximum size of the L2 table cache
"refcount-cache-size": maximum size of the refcount block cache
"cache-size": maximum size of both caches combined

There are a few things that need to be taken into account:

 - Both caches must have a size that is a multiple of the cluster size
   (or the cache entry size: see "Using smaller cache sizes" below).

 - The maximum L2 cache size is 32 MB by default on Linux platforms (enough
   for full coverage of 256 GB images, with the default cluster size). This
   value can be modified using the "l2-cache-size" option. QEMU will not use
   more memory than needed to hold all of the image's L2 tables, regardless
   of this max. value.
   On non-Linux platforms the maximal value is smaller by default (8 MB) and
   this difference stems from the fact that on Linux the cache can be cleared
   periodically if needed, using the "cache-clean-interval" option (see below).
   The minimal L2 cache size is 2 clusters (or 2 cache entries, see below).

 - The default (and minimum) refcount cache size is 4 clusters.

 - If only "cache-size" is specified then QEMU will assign as much
   memory as possible to the L2 cache before increasing the refcount
   cache size.

 - At most two of "l2-cache-size", "refcount-cache-size", and "cache-size"
   can be set simultaneously.

Unlike L2 tables, refcount blocks are not used during normal I/O but
only during allocations and internal snapshots. In most cases they are
accessed sequentially (even during random guest I/O) so increasing the
refcount cache size won't have any measurable effect in performance
(this can change if you are using internal snapshots, so you may want
to think about increasing the cache size if you use them heavily).

Before QEMU 2.12 the refcount cache had a default size of 1/4 of the
L2 cache size. This resulted in unnecessarily large caches, so now the
refcount cache is as small as possible unless overridden by the user.

Using smaller cache entries
---------------------------
The qcow2 L2 cache can store complete tables. This means that if QEMU
needs an entry from an L2 table then the whole table is read from disk
and is kept in the cache. If the cache is full then a complete table
needs to be evicted first.

This can be inefficient with large cluster sizes since it results in
more disk I/O and wastes more cache memory.

Since QEMU 2.12 you can change the size of the L2 cache entry and make
it smaller than the cluster size. This can be configured using the
"l2-cache-entry-size" parameter:

   -drive file=hd.qcow2,l2-cache-size=2097152,l2-cache-entry-size=4096

Since QEMU 4.0 the value of l2-cache-entry-size defaults to 4KB (or
the cluster size if it's smaller).

Some things to take into account:

 - The L2 cache entry size has the same restrictions as the cluster
   size (power of two, at least 512 bytes).

 - Smaller entry sizes generally improve the cache efficiency and make
   disk I/O faster. This is particularly true with solid state drives
   so it's a good idea to reduce the entry size in those cases. With
   rotating hard drives the situation is a bit more complicated so you
   should test it first and stay with the default size if unsure.

 - Try different entry sizes to see which one gives faster performance
   in your case. The block size of the host filesystem is generally a
   good default (usually 4096 bytes in the case of ext4, hence the
   default).

 - Only the L2 cache can be configured this way. The refcount cache
   always uses the cluster size as the entry size.

 - If the L2 cache is big enough to hold all of the image's L2 tables
   (as explained in the "Choosing the right cache sizes" and "How to
   configure the cache sizes" sections in this document) then none of
   this is necessary and you can omit the "l2-cache-entry-size"
   parameter altogether. In this case QEMU makes the entry size
   equal to the cluster size by default.

Reducing the memory usage
-------------------------
It is possible to clean unused cache entries in order to reduce the
memory usage during periods of low I/O activity.

The parameter "cache-clean-interval" defines an interval (in seconds),
after which all the cache entries that haven't been accessed during the
interval are removed from memory. Setting this parameter to 0 disables this
feature.

The following example removes all unused cache entries every 15 minutes:

   -drive file=hd.qcow2,cache-clean-interval=900

If unset, the default value for this parameter is 600 on platforms which
support this functionality, and is 0 (disabled) on other platforms.

This functionality currently relies on the MADV_DONTNEED argument for
madvise() to actually free the memory. This is a Linux-specific feature,
so cache-clean-interval is not supported on other systems.

Extended L2 Entries
-------------------
All numbers shown in this document are valid for qcow2 images with normal
64-bit L2 entries.

Images with extended L2 entries need twice as much L2 metadata, so the L2
cache size must be twice as large for the same disk space.

   disk_size = l2_cache_size * cluster_size / 16

i.e.

   l2_cache_size = disk_size * 16 / cluster_size

Refcount blocks are not affected by this.